## Slide 1: Virtual machines
Inf-2201, University of Tromsø, Spring 2018
Lars Ailo Bongo
Lars.ailo.bongo@uit.no
Including slides from Andy Bavier, Princeton University

## Slide 2: Cloud Computing
Utility computing: on-demand provision of storage and compute resources over a network
Key concepts:
  Customers pays for as little or much resources as they need (elasticity)
  Vendors goal is to optimize resource utilization  run multiple clients on same machine
  Service level agreement regulates quality of service
How to share a machine and offer required protection?

## Slide 3: Datacenter Workload
Source: The Impact of Management Operations on the Virtualized Datacenter. Soundararajan and Anderson. ISCA’10.

## Slide 4: Virtual Machine Monitors (VMM)
Layer below the operating system
Presents hardware interface to an OS
Multiplexes resources between several virtual machines (VMs)
Isolates VMs from each other
  Separate address spaces
  Performance isolation (to some degree)

## Slide 5: VM/370 with CMS
VM/370: VMM
CSM: an advanced shell

## Slide 6: History
Have been around since the 1960’s on mainframes
  VM/370: used for multitasking
Resurfaced on commodity platforms in 2000’s
  Server consolidation
  Web hosting centers
  Managed desktop/ thin-client/ browsers
  Software development (such as kernels)
  Linux in Windows
  Cloud computing

## Slide 7: Design Issues
Manageability
  Ease of maintenance, administration, provisioning, etc
Performance
  Minimize overhead of virtualization
Isolation
  Data of one VM should not be accessible from others (security)
  Activity of one VM should not impact other VMs (performance isolation)
Scalability
  Minimize cost per VM

## Slide 8: Processor Virtualization
Popek and Goldberg (1974)
  Sensitive instructions: only executed in kernel mode
  Privileged instructions: trap when run in user mode
  CPU architecture is virtualizable only if sensitive instructions are subset of privileged instructions
  When guest OS runs a sensitive instruction, must trap to VMM so it maintains control

## Slide 9: VMM Types

## Slide 10: Virtualization Styles
Fully virtualizing VMM
Para-virtualizing VMM
  Requires changes to host OS

## Slide 11: Type 1 Hypervisors

## Slide 12: Revisit Microkernels
How does a microkernel differ from a Type 1 Hypervisor?

## Slide 13: Classic Microkernel Paper
Describes how to implement an efficient microkernel
Measures overhead of running Linux on top of L4 microkernel
(Prof. Härtig was a good friend of the department)

## Slide 14: “Are Virtual Machines Microkernels Done Right?”
HotOS’05 paper by Hand, et. Al.
  (note! HotOS papers are often written to be controversial)
Claim that VMM are better since they
  Kernel is not dependent on user level components
  Make IPC performance irrelevant
  Treat the OS as component
Do you agree?
What will the future bring?

## Slide 15: Paravirtualization

## Slide 16: Paravirtualization (2)

## Slide 17: VMM Classification

## Slide 18: VMM Implementation
Efficiently virtualize the hardware
  Provide illusion of multiple machines
  Retain control of the physical machine
Subsystems
  Processor Virtualization
  Memory Virtualization
  I/O virtualization

## Slide 19: x86 Processor Virtualization
x86 architecture is not fully virtualizable
  Certain privileged instructions behave differently when run in unprivileged mode
  Certain unprivileged instructions can access privileged state
Techniques to address inability to virtualize x86
  Static replacement of non-virtualizable instructions with easily virtualized instructions (Para-virtualization)
  Perform binary translation (Full Virtualization)
Since 2005 (Intel) and 2006 (AMD): HW virtualization support

## Slide 20: Memory Virtualization
Traditional way is to have the VMM maintain a shadow of the VM’s page table
The shadow page table controls which pages of machine memory are assigned to a given VM
When guest OS updates its page table, VMM updates the shadow page table

## Slide 21: I/O Virtualization
Issue: lots of I/O devices
  Problem: Writing device drivers for all I/O device in the VMM layer is not a feasible option
Insight: Device driver already written for popular Operating Systems
Solution: Present virtual I/O devices to guest VMs and channel I/O requests to a trusted host VM running popular OS

## Slide 22: I/O Virtualization

## Slide 23: IBM VM/370
Type 1, fully virtualized
HW, VMM, and guest OS co-designed
Released in 1972
Successor z/VM still in use today on mainframes
It provides: “multiple software replicas of real computing systems on one real processor” [Seawright and Mackinnon, 1979]

## Slide 24: “Usefulness of VM/370”
Run multiple versions of an OS
Test upgrades to an OS
Backward compability for old applications
System integrity and isolation
Computer science “laboratory”

## Slide 25: VM/370: Memory and I/O Virtualization
Memory virtualization:
  Each virtual machine has separate address space
  CP (VMM) has no dynamic paging
I/O Virtualization:
  Physical disk divided into continuous cycles (minidisk)
  Each VM has separate minidisk
  Access control implemented for minidisks
Host operating systems rewritten to use VMM
Hardware support for VMM operations

## Slide 26: VMware ESX Server
Type I VMM - Runs on bare hardware
Full-virtualized – Legacy OS can run unmodified on top of ESX server
Fully controls hardware resources and provides good performance
Enterprise solution

## Slide 27: ESX Server – CPU Virtualization
Most user code executes in Direct Execution mode; near native performance
Runtime Binary Translation for x86 virtualization
  Privileged mode code is run under control of a Binary Translator, which emulates privileged instructions
  Fast compared to other binary translators as source and destination instruction sets are nearly identical
Can binary translated code outperform HW supported code?

## Slide 28: ESX Server – Memory Virtualization
Maintains shadow page tables with virtual to machine address mappings.
Shadow page tables are used by the physical processor
ESX maintains the pmap data structure for each VM with “physical” to machine address mappings
ESX can easily remap a machine page

## Slide 29: ESX Server – Memory Management
Page reclamation – Ballooning technique
  Reclaims memory from other VMs when memory is overcommitted
Page sharing – Content based sharing
  Eliminates redundancy and saves memory pages when VMs use same operating system and applications

## Slide 30: ESX Server- Ballooning

## Slide 31: ESX Server – Page Sharing

## Slide 33: ESX Server – I/O Virtualization
Has highly optimized storage subsystem for networking and storage devices
  Directly integrated into the VMM
  Uses device drivers from the Linux kernel to talk directly to the device
Low performance devices are channeled to special “host” VM, which runs a full Linux OS

## Slide 34: ESXi Architecture

## Slide 35: VMkernel
(from ESXi Architecture white paper)
POSIX-like operating system
  Process creation and control, signals, file system, process threads…
Designed to support multiple virtual machines
  Simple in-memory file system (configuration files, logs, patches)
  User and groups (management and administration)
  “User worlds”: limited POSIX framework to run hypervisor

## Slide 36: VMware Workstation
Type II VMM - Runs on host operating system
Full-virtualized – Legacy OS can run unmodified on top of VMware Workstation
Appears like a process to the Host OS
Free version: WMware player

## Slide 37: Workstation - Virtualization
CPU virtualization and memory virtualization
  Uses Similar Techniques as the VMware ESX server
I/O Virtualization
  Workstation relies on the Host OS for handling I/O requests
  I/O incurs overhead as it has to switch to the Host OS on every IN/OUT instruction.

## Slide 38: Workstation – I/O Virtualization
VMM must be able to intercept all I/O operations issued by the Guest OS
These are trapped by the VMM and emulated either in VMM or VMApp.
Any access that interact with physical hardware have to be handled by VMApp
I/O intensive workload performs poorly due to extra host switches between the Host and the VMM worlds

## Slide 39: Workstation – Virtualize NIC

## Slide 40: VMM Hardware Support
CPU virtualization support:
  Intel VT introduced in 2005 and AMD-V introduced in 2006
Memory management support:
  Extended page tables
I/O MMU virtualization
  Intel VT-d and AMD-Vi
  Network virtualization: Intel VT-c
Most VMMs utilize HW support

## Slide 41: CPU Virtualization Support
Virtual machine control block (VMCB): control state with subset of the guest virtual CPU
Less privileged execution mode: guest mode
New instruction vmrun executed by VMM:
  HW loads guest state from VMCB and switches to guest mode
  Run until some condition expressed by VMCB is reached
Exit from guest mode:
  HW saves guest state in VMCB
  HW loads VMM supplied state to HW
  Resume executing VMM

## Slide 42: MMU Support
Extended page tables (EPT):
  Ordinary pages tables: virtual to guest-physical addresses
  EPT: guest-physical to host-physical addresses
TLB entries map virtual to host-physical addresses

## Slide 43: EPT - TLB Miss
Miss on virtual address V
Use guest table pointer (cr3) to locate guest page directory
Map guest-cr3 address to host-physical address by walking nested page tables
Read page table entry in guest page directory
Map guest page table address to physical memory
Read guest-physical address in page table
Map guest-physical to host host-physical address
Resume execution

## Slide 44: Intel VT for Directed I/O
(from Intel VT for Directed I/O – Architecture Specification)
I/O device assignment: for flexibly assigning I/O devices to VMs and extending the protection and isolation properties of VMs for I/O operations.
DMA remapping: for supporting independent address translations for Direct Memory Accesses (DMA) from devices.
Interrupt remapping: for supporting isolation and routing of interrupts from devices and external interrupt controllers to appropriate VMs.
Reliability: for recording and reporting to system software DMA and interrupt errors that may otherwise corrupt memory or impact VM isolation.

## Slide 45: Xen
Type I VMM
  Para-virtualized
  Open-source
  Designed to run 100s of virtual machines on a single machine
Commercial version: Citrix Xen

## Slide 46: Xen – CPU Virtualization
Privileged instructions are paravirtualized by requiring them to be validated and executed with Xen
Processor Rings
  Guest applications run in Ring 3
  Guest OS runs in Ring 1
  Xen runs in Ring 0
Guest OS code must modified

## Slide 47: Xen – Memory Virtualization
Initial memory allocation is specified and memory is statically partitioned
A maximum allowable reservation is also specified.
Balloon driver technique similar to ESX server used to reclaim pages
Guest OS is responsible for allocating and managing hardware page table
Xen involvement is limited to ensure safety and isolation
Xen exists in the top 64 MB section at the top of every address space to avoid TLB flushes when entering and leaving the VMM

## Slide 48: Xen – I/O Virtualization
Xen exposes a set of clean and simple device abstractions
I/O data is transferred to and from each domain via Xen, using shared memory, asynchronous buffer descriptor rings
Xen supports lightweight event delivery mechanism used for sending asynchronous notifications to domains

## Slide 49: Other VMMs
Microsoft Hyper-V
Oracle VirtualBox
  Type 2, fully virtualized
  Open source
  Nice documentation
Is bochs a virtual machine?
Other?

## Slide 50: Summary
Cloud as motivation for virtualization
Virtual machine monitor design and classification
  Type 1 vs. Type 2
  Fully virtualized vs. paravirtualized
Design of different VMMs

## Slide 51: References
Data center workload
L4 paper
HotOS paper
VM/370 paper (VM/370 – a study of multiplicity and usefulness)
VMWare paper
Xen paper
VMWare ESXi whitepaper